Current Source

# Maxim's Design
Built into a small 2.6" x 2" x 1.6" box. Put a double throw (one side momentary, one side on) switch to power the 9 volt battery. Also put a slide switch to allow future expansion to supplying e.g. 10 mA also. Used dual banana plug for output. 9 V and C cell inside for power. Small chunk of PC board 2" x 2" for components. Found some nice HP 0.4  resistors that don't change when 1 A goes through them; put 2 in parallel to make 0.2  shunt to measure 1 A current.
Using a "9 V" wall wart for power (actual voltage = 13.79 V), I got the following voltages in the circuit with respect to ground (- side of 9 V battery): pin 6 of MAX872 = 2.4988 V, pin 3 of op amp = 200.97 mV, pin 2 of op amp = 201.27, pin 6 of op amp = 3.759 V.
The circuit comes up to a stable 1.000 A of current in 1.2 ms as measured by a scope. Since most measurements will only take a few seconds, the C battery should last a long time. Assuming the battery's capacity at this current level will be about half of the rated 8300 mA*hr, that means roughly 4 hours of operation. At 5 seconds per measurement, that means more than 2500 measurements.
The IRF3205 MOSFET gets warm to the touch at steady state of 1 A; I measured the temperature with my IR thermometer as 120 °F = 49 °C. This is acceptable, as the junction to ambient thermal resistance is 62 °C/W. The voltage across the MOSFET drain to source at 1 A was 0.602 V, meaning the power was 0.6 W. Thus, the junction temperature was around 80 °C; the datasheet says the maximum is 175 °C. I plan to put a piece of tape over it to insulate its leads and not worry about any heat sink.
The output current seems to vary from 999 mA to 1000 mA on startup and steady state. This is 0.1% accuracy, which is fine for the portable use intended.
Here's the modified schematic that was used:
Note the MOSFET is the IRF3205, not the IRF540. All resistors are 1/4 W carbon film except for the 0.2 ohm, which is made from two 0.4 ohm wirewound HP resistors. The pot is a 100 k Bourns Trimpot.
The GR resistance box was used to find the resistance values needed in addition to the 0.2 ohm resistance to get the following current levels:
I could solder in some kind of fixture to hold two wires that connected to a resistor, then keep a small bag of the appropriate resistors in a small bag. This would allow me to choose the second current level by opening the box and plugging the appropriate resistor in.
The resistor program gives me the following choices to make up these resistances:
Value	Series	Parallel
11.8	No match	12 and 680
127.6	17.8 and 110	170 and 513
2810	196 and 2.61 k	3 k and 46 k
12.8 k	1 k and 11.8 k	13.3 k and 330 k
134.7 k	15 k and 120 k	150 and 1.33 k

I would prefer the parallel form over the series because the two resistor's ends will be soldered together and two wires will be led out for connections. This allows a compact package by just wrapping in some tape.
The red 14 pin sockets I have would be nice for this application because the 24 gauge solid copper telephone wire fits in them perfectly. You do have to tie a knot in the wire to avoid insulation slipping on the wire.
I soldered in the C cell and installed the 9 V battery. Vinyl tape went over PC board edges and switches to insulate things and I closed up the box. I've not installed the lower current resistor yet, so the slide switch doesn't work. I'll check its output on the HP3435 for a day or so. So far, it comes up reading exactly 1000 mA each time I've tried, even as the 3435's zero reading drifts to -001. I've found that if I turn off the 3435, it maintains its zero better immediately after you turn it on.
24 May 2011 note: I built this circuit in March 2011 and have now used it a number of times for making low resistance measurements. It's quite useful and has been very stable (I have reason to believe my HP 3435 ammeter might vary a bit more than this current source does). I am still very pleased with how it is in such a small box. I also built a 1 A current source from an LM317 that runs from line power, but it almost never gets used because this little one is so handy.
# Using LM317
(Probably straight from the datasheet)
This works, but is not ideal. The IC dissipates quite a bit of power so needs to be on a good heat sink. The current also varies a bit over time.
# Shunt current source
Drawn by Andrew Morris. Current out is 0.6/R2 volts.

# Transistor current source
See http://en.wikipedia.org/wiki/Current_source#Current_sources_with_series_negative_feedback

DZ1 is a zener diode which, when reverse biased (as shown in the circuit) has a constant voltage drop across it irrespective of the current flowing through it. Thus, as long as the zener current (IZ) is above a certain level (called holding current), the voltage across the zener diode (VZ) will be constant. Resistor R1 supplies the zener current and the base current (IB) of NPN transistor (Q1). The constant zener voltage is applied across the base of Q1 and emitter resistor R2. The operation of the circuit is as follows:
Voltage across R2 (VR2) is given by VZ - VBE, where VBE is the base-emitter drop of Q1. The emitter current of Q1 which is also the current through R2 is given by
alignc {I_{R2} `=` I_E `=` {V_{R2}} over {R2} `=` {V_Z - V_{BE}} over {R2}}
Since VZ is constant and VBE is also (approximately) constant for a given temperature, it follows that VR2 is constant and hence IE is also constant. Due to transistor action, emitter current IE is very nearly equal to the collector current IC of the transistor (which in turn, is the current through the load). Thus, the load current is constant (neglecting the output resistance of the transistor due to the Early effect) and the circuit operates as a constant current source. As long as the temperature remains constant (or doesn't vary much), the load current will be independent of the supply voltage, R1 and the transistor's gain. R2 allows the load current to be set at any desirable value and is calculated by
R2 `=` {V_Z - V_{BE}} over {I_{R2}} `=` {V_Z - 0.65} over {I_{R2}}
the latter for a silicon device.
(IR2 is also the emitter current and is assumed to be the same as the collector or required load current, provided hFE is sufficiently large). Resistance R1 at resistor R1 is calculated as
R_1 `=` {V_S - V_Z} over {I_Z + K cdot I_B}
where K = 1.2 to 2 (so that R1 is low enough to ensure adequate IB),
I_B `=` {I_C "(=" I_E "=" I_{R2} ")"} over {h_{FE(min)}}
and hFE(min) is the lowest acceptable current gain for the particular transistor type being used.
The Zener diode can be replaced by any other diode, e.g. a light-emitting diode LED1 as shown in Figure 5. The LED voltage drop (VD) is now used to derive the constant voltage and also has the additional advantage of tracking (compensating) VBE changes due to temperature. R2 is calculated as
R_2 `=` {V_D - V_{BE}} over {I_{R2}}
and R1 as
R_1 `=` {V_S - V_D} over {I_D + K cdot I_B}
where ID is the LED current.
## Diode compensation
See http://en.wikipedia.org/wiki/Current_source#Transistor_current_source_with_diode_compensation
Temperature changes will change the output current delivered by the circuit of Figure 3 because VBE is sensitive to temperature. Temperature dependence can be compensated using the circuit of Figure 4 that includes a standard diode D (of the same semiconductor material as the transistor) in series with the Zener diode as shown in the image on the left. The diode drop (VD) tracks the VBE changes due to temperature and thus significantly counteracts temperature dependence of the CCS.
Resistance R2 is now calculated as
R_2 `=` {V_Z + V_D - V_{BE}} over {I_{R2}}
Since VD = VBE = 0.65 V,
R_2 `=` V_Z over {I_{R2}}
(In practice VD is never exactly equal to VBE and hence it only suppresses the change in VBE rather than nulling it out.)
R1 is calculated as
R_1 `=` {V_S - V_Z - V_D} over {I_Z + K cdot I_B}
(the compensating diode's forward voltage drop VD appears in the equation and is typically 0.65 V for silicon devices.)
This method is most effective for Zener diodes rated at 5.6 V or more. For breakdown diodes of less than 5.6 V, the compensating diode is usually not required because the breakdown mechanism is not as temperature dependent as it is in breakdown diodes above this voltage.
# Op amp current source
http://en.wikipedia.org/wiki/Current_source
Another common method is to use a negative feedback to set the current and remove the dependence on the Vbe of the transistor. The figure shows a common approach using an op amp with the non-inverting input connected to a voltage source (such as the Zener in an above example) and the inverting input connected to the same node as the resistor and emitter of the transistor. The circuit is actually a non-inverting amplifier driven by a constant input voltage. It keeps up this constant voltage across the constant sense resistor; as a result, the current flowing through the load is constant as well. The article on current mirror discusses another example of these so-called gain-boosted current mirrors.

# AAC current source
http://forum.allaboutcircuits.com/album.php?albumid=26&pictureid=1321

Current is 0.6/R1.
# Current source/mirror
From http://www.4qdtec.com/csm.html

Circuit 1
This is about the simplest current source possible. It is essentially an emitter follower where the transistor's Vbe is used to define the current through R2. If R2 is chosen so that the current through it is much more than the the transistor's base current, then ib can be ignored and the current through R3 (the load) is Vb/R2.
The same circuit is also used as a Vbe multiplier - when R3 is connected B-C of the transistor. As iR2 = iR3 the voltage between c-e is the transistor is Vbe x (R2+R3) / R2
Circuit 2
This is a very standard current source. Vin causes a current to flow through R1 into the diode. So a voltage is developed across the diode. This voltage is also present across the base-emitter junction of the transistor, so a current must flow in the transistor. The magnitude of the transistor current depends on the voltage developed across the diode and this is a function of its geometry. So the ratio of input to output current is not easy to calculate. However it will be pretty consistent with identical diodes and transistors because modern production causes very little spread in device parameters. The base-emitter junction of a transistor behaves just like a diode.
Circuit 3
Instead of a diode, you can use an LED. An LED (depending on colour, intensity etc) drops about 2v so you can calculate the output current as shown.
Circuit 4
This is a commonly used source: Vin drives current through R1 into the base of the second transistor, so current flows into the transistor's collector, through it and out of its emitter. This current must flow through R2. If the current gets too high, the first transistor turns on and robs the second transistor of base current, so its collector current can never exceed the value shown. This is an excellent way of either making a current source or of limiting the available current to a defined maximum value.
Circuit 5
This is a true current mirror: feed a current (i1) into the first transistor (usually by driving it via a resistor from a suitable voltage) and a 'mirror' current (i2) flows in the second transistor. Provided the two transistors are matched and of high gain, input and mirror current will match quite closely. In fact, with modern transistors, if you use a -C gain rating (450-900) matching of any two transistors is probably adequate for all usual needs.
Look at the equivalent circuit of virtually any analogue IC and you will notice this type of current source/mirror (it may be used for either) but it works just as well with discrete transistors.
One source of errors is if the voltage across the output transistor is high enough to cause the transistor to heat: the mirror's performance fails because the two transistors are now no longer well matched!
This circuit can also be used with resistors in both emitters - in this case the mirror ratio will depend on the ratio of these resistors. An example of this.
Circuit 6
This is for the purists: circuit 4 gives an error due to the base bias current. Here is the commonest way of reducing this error. It gives significantly improved performance.
Circuit 7
This is another way of reducing the error but this circuit is not quite so commonly known. If you calculate the formulae using practical transistors (beta = 500 or so) both 5 and 6 give very close matching - but 6 is slightly better. An example of this.
However there is a problem which sometimes occurs on current mirrors: if the output current is flowing from a significantly high voltage (Vc), then there may be enough power (Vc x i²) in the output transistor of figure 5 to cause the transistor to get warm: heating destroys the balance between the two transistors and so destroys the mirror's accuracy. In circuit 6 any heating is in the third transistor (at the top) and it is not part of the mirror so the mirror ratio is not affected by heating in this transistor. See 'Useful facts' below.
Circuit 8
Just to prove that I can use ICs, here is a current source (or a voltage to current converter) using an IC. You can use a single transistor (the PNP one) but the transistor's base current slightly alters the ratio. You can of course use an FET (zero gate current) but these are relatively expensive. Here is a complimentary long tailed pair biased to cancel out base current errors. Very good - provided you have a suitable bias point for Vb!
Circuit 9
One of the problems with circuits 2,3,4,5 and 6 is heating in the output transistor - a problem which was solved in circuit 7. Here's another way of avoiding heating causing an error - this circuit uses a cascode arrangement so that the current is defined in the bottom transistor, which has very little voltage across it. The top transistor has any high voltage across it, but heating in the top transistor doesn't affect the current, as it's the bottom transistor that is defining it.