cut.py
someonesdad1@gmail.com 29 Dec 2012

The cut.py program is a python console-based script that will generate a solution to a one-dimensional stock cutting problem. For a plethora of information on the problem, do a web search on the term "one-dimensional stock cutting problem", as it's an important commercial problem when raw materials need to be cut.
The cut.py script uses the first fit decreasing heuristic, which has been well-studied and is straightforward to program -- and is roughly the approach you'd take if you were solving the problem manually. It is not guaranteed to find the best solution, but it seems to work reasonably well.
The first fit decreasing method sorts the set of lengths desired and the set of stock material, then selects the largest piece to be cut and cuts it from the smallest stock piece available. Repeat until there are no more stock pieces or the remaining stock is too small to cut a required piece. An important part of the script is that all lengths are converted to integers by dividing by the resolution given in the datafile (defaults to 1) and taking the integer part. This allows exact arithmetic, which avoids annoying roundoff problems when using floating point numbers.
If you wish to use the cut.py script to solve problems, you'll first have to load python on your computer. You can go to http://www.python.org/ and download a copy of python. You'll need to get the latest 2.6 or 2.7 versions, as the cut.py script doesn't work with python 3. While it could be made to work with python 3, it would take more work than I was willing to invest (I'm still using python 2.6.5 because of many dependencies I have on older libraries). I've run the example scripts given here with both python 2.6.5 and 2.7.2.
This program is aimed at hobbyists working in a shop. More sophisticated freeware and commercial solutions can include a number of other constraints in solving the problem. It's worth looking at the paper by Haessler and the wikipedia page [wp] to get a feel for the similar problems that are important in industry.
# Installation
Unzip the cut.zip package and run the cut.py script by the command
python cut.py
If you see the usage message, then the script should be ready to run. You can move the sig.py and odict.py modules to a directory in your PYTHONPATH if you wish.
The files in the package are cut.py, cut.pdf (i.e., this document), sig.py, and odict.py.
# Examples
Here's the usage statement of the script (run it with no command line parameters):
Usage: cut.py [options] datafile
  Generate a cutting list for parts that must be cut from lengths of
  raw materials. The datafile contains the information used to define
  the problem. The algorithm used is the first fit decreasing
  heuristic, which picks the largest piece which needs to be cut and
  selects the smallest remaining stock piece to cut it from.

  -c Print a datafile template to stdout (use in conjunction with
        -v option to get a verbose template with explanations of each
        item needed).
  -v Turn verbose printing on (shows the input data).
One of the first rules of testing a new computer program is to have it solve a problem you know the answer to. If it falls on its face doing that problem, it's probably not worth keeping.
## Simple problem
A simple problem is generated from the datafile template that is output when you type the command
python cut.py -c
This yields the template for a sample datafile:
sigfig = 3
kerf = 1
resolution = 0.1
stock = 2, 100
piece = 9, 10
pieces = 10, 20, 29, 30
Note: when you're just starting out with the cut.py script, use the -c -v command line options to get a datafile template that has comments explaining what each item in the datafile is.
We can solve this problem by inspection. The 9 stock pieces 10 units long will consume 90 units of a 100 unit stock piece. Since there will be 9 cuts to get these raw material pieces, we add in the length of 9 kerfs. Thus, the first stock piece is used except for a 1 unit piece of scrap[1].
[1] Yes, I know, in reality that last 1 unit of length will be consumed in cutting the last piece to length.
The remaining four pieces of 10, 20, 29, and 30 units long result in a use of 89 units plus 4 for the kerfs, or 93 units used with a scrap of 7. Thus, the total scrap is 8 out of the 200 units of stock or 4%.
Note that the algorithm we just used is not the same as the first fit decreasing. Let's solve the problem with the first fit decreasing heuristic. The sorted pieces are:
10, 10, 10, 10, 10, 10, 10, 10, 10, 10, 20, 29, 30
and the sorted stock lengths are
100 100
Pick the smallest stock to get 100. The largest piece we can cut from this is 30, leaving 69 (allowing for the kerf). Then cut 29 from this (because it's the smallest stock piece) to leave a remainder of 39. We can cut the 20 and 10 lengths from this too, leaving a scrap piece of 7.
The remaining 9 pieces of length 10 result in all but 1 unit being used from the second stock piece of 100. Thus, we're left with a scrap of 8. Since we started with a total stock length of 200, the script reports this as a scrap percentage of 100(8)/200 or 4%. If we put the above template data into the file datafile and run the command
python cut.py datafile
we get the output
Cutlist ([x] is scrap length, {n} is count) Kerf = 1.00
  Total scrap = 8.0 (4.0% of total stock)
  100.0: 10.0, 10.0, 10.0, 10.0, 10.0, 10.0, 10.0, 10.0, 10.0 [1.0]
  100.0: 10.0, 20.0, 29.0, 30.0 [7.0]
Note that the two different algorithms we just used gave the same answers; apparently such degeneracy is relatively common for these cutting problems.
You didn't see any numbers in curly braces in this problem (indicating a count), but you'll see them in the next problem.
## A bigger problem
The video at [lec4] gives the problem of cutting pieces from stock lengths of 20; here's the datafile:
stock = 622, 20
piece = 511, 9
piece = 301, 8
piece = 263, 7
piece = 383, 6
If they're not given in the datafile, the resolution defaults to unity and the kerf width defaults to zero. The results are:
Cutlist ([x] is scrap length, {n} is count) Kerf = 0.000
  Total scrap = 1294 (10% of total stock)
  20{131}: 6, 7, 7 [0]
  20: 6, 6, 7 [1]
  20{83}: 6, 6, 6 [2]
  20{255}: 9, 9 [2]
  20: 8, 9 [3]
  20{150}: 8, 8 [4]
  20: 6 [14]
I haven't taken the time to watch the videos to see the answer determined in the lecture, so I don't know how close this answer is to a more optimum one. Considering that the python script only takes a few seconds to generate the answer, it seems reasonable to me. However, if the problem was being done in industry, other constraints would probably apply and could justify using a commercial tool to generate better solutions.
## Another problem
Here's another problem I made up by generating some uniformly-distributed integers:
kerf = 0.2
resolution = 0.1
stock = 42, 100
pieces = 84, 76, 42, 26, 51, 41, 78, 31, 48, 58, 90, 50, 28, 75, 62
pieces = 25, 91, 98, 81, 90, 31, 73, 89, 68, 47, 10, 43, 61, 91, 96, 48, 86
pieces = 26, 80, 55, 2, 72, 40, 82, 67, 1, 49, 86, 25, 33, 87, 19, 57, 24, 96
pieces = 80, 45, 8, 32, 51, 93, 11, 55, 70, 55, 81, 54, 96, 60, 59, 45, 60, 39
Here's the solution from the script:
Cutlist ([x] is scrap length, {n} is count) Kerf = 0.2
  Total scrap = 323.4 (7.7% of total stock)
  100.0: 1.0, 2.0, 96.0 [0.4]
  100.0: 19.0, 25.0, 55.0 [0.4]
  100.0: 8.0, 91.0 [0.6]
  100.0: 10.0, 89.0 [0.6]
  100.0: 24.0, 75.0 [0.6]
  100.0: 26.0, 73.0 [0.6]
  100.0: 31.0, 68.0 [0.6]
  100.0: 32.0, 67.0 [0.6]
  100.0: 39.0, 60.0 [0.6]
  100.0: 40.0, 59.0 [0.6]
  100.0: 41.0, 58.0 [0.6]
  100.0: 42.0, 57.0 [0.6]
  100.0: 45.0, 54.0 [0.6]
  100.0{2}: 48.0, 51.0 [0.6]
  100.0: 49.0, 50.0 [0.6]
  100.0: 11.0, 87.0 [1.6]
  100.0: 26.0, 72.0 [1.6]
  100.0: 28.0, 70.0 [1.6]
  100.0: 43.0, 55.0 [1.6]
  100.0: 98.0 [1.8]
  100.0{2}: 96.0 [3.8]
  100.0: 33.0, 62.0 [4.6]
  100.0: 93.0 [6.8]
  100.0: 31.0, 61.0 [7.6]
  100.0: 45.0, 47.0 [7.6]
  100.0: 91.0 [8.8]
  100.0{2}: 90.0 [9.8]
  100.0{2}: 86.0 [13.8]
  100.0: 25.0, 60.0 [14.6]
  100.0: 84.0 [15.8]
  100.0: 82.0 [17.8]
  100.0{2}: 81.0 [18.8]
  100.0{2}: 80.0 [19.8]
  100.0: 78.0 [21.8]
  100.0: 76.0 [23.8]
  100.0: 55.0 [44.8]
It's not clear to me that this is a solution near to optimal. I look at the latter entries in the table and wonder if better cutting choices would lead to a lower scrap percentage -- but it would take a better algorithm or more insight than I can bring to the problem. And, in all honesty, such a problem is probably beyond anything I would need in my shop, so it's not worth my time to code up a better algorithm.
## Fractions
If you prefer to use fractional measurements for stock or piece dimensions, you can. If the resolution in the datafile is given as an improper fraction, then the output will be in terms of such fractions. Thus, for the following datafile:
kerf = 1/8
resolution = 1/16
stock = 3, 96
piece = 8, 19+1/4
pieces = 2+13/16, 7+1/16, 87+1/2
you'll get the output
Cutlist ([x] is scrap length, {n} is count) Kerf = 1/8
  Total scrap = 35+1/4 (12.2500% of total stock)
  96: 7+1/16, 87+1/2 [1+3/16]
  96: 2+13/16, 19+1/4, 19+1/4, 19+1/4, 19+1/4 [15+9/16]
  96: 19+1/4, 19+1/4, 19+1/4, 19+1/4 [18+1/2]
If you're wondering why the scrap percentage is given to 6 significant figures, it's because the template rounding feature of sig.py used the fraction 1/16 -- which is 0.0625.
# References
These are programs/references that I found while studying this problem. I haven't tried the programs and can make no recommendations concerning them.
klotz	http://www.myvirtualnetwork.com/mklotz/. Look at his cuts.zip file.
wp	http://en.wikipedia.org/wiki/Cutting_stock_problem http://en.wikipedia.org/wiki/Subset_sum_problem
maxcut	http://www.maxcut.co.za/
delphi	http://www.delphiforfun.org/Programs/Cutting%20Stock.htm
su	http://lumberjocks.com/topics/9435. A plug-in for Google SketchUp.
haessler	http://deepblue.lib.umich.edu/bitstream/2027.42/30249/1/0000644.pdf / R. Haessler, One-Dimensional Cutting Stock Problems and Solution Procedures, Math. Comput. Modelling, Vol 16, No. 1, pp 1-8, 1992.
lec4	http://www.youtube.com/watch?v=NoiPrt4OsQA A video lecture.